## Slide 1: COMP90018 Mobile Computing Systems Programming
Prof. Vassilis Kostakos

## Slide 2: Introduction to LBS
Location-based services (LBS)
  Services that integrate a mobile’s device location with other information
  Available at least since the 1970s (GPS: US military)
Mobile operators
  Voice, data (SMS, MMS, Video), location information
Push versus pull
  User receives information without an active request
  User actively pulls information from the network

## Slide 3: Applications I
Infotainment services
  Driving directions
  Where is a point of interest (POI): ATM, hotel, restaurant, …
  Where am I? Location on a map
  Where are my friends?
Tracking services
  Fleet management, taxi monitoring and dispatching
  Children, elderly people, sick persons
  Goods and package tracking

## Slide 4: Applications II
Information dissemination services
  Content delivery wrt. the user’s context & profile
  Advertisement & e-coupons
  Hazard warnings
Emergency support systems
  Police, ambulance, fire brigades
  Roadside assistance
Location-sensitive billing
  Call billing based on vicinity from base/home
  Toll payment

## Slide 5: AT&Ts Find Friend
User interface
  User can add friends to a list
  Send a SMS with a tracking request
Privacy
  “Invisible” mode allows to hide from all users
  Tracking requests always generated an alert
Services
  Driving directions or meeting point between friends
  Search for all friends

## Slide 6: Location-based Services
1st Generation
  Manual user input of location information
  Driving directions, nearby POIs, weather information
2nd Generation
  Location information is acquired automatically within a couple of kilometers
  Similar services as in 1st generation
3rd Generation
  High position accuracy & automatic initiation of services
  Asset tracking, street-level routing and positioning, …

## Slide 7: Localisation technologies
Location enables a variety of ubicomp applications providing services appropriation to specific location and context
  Routing phone calls to phone closest to user’s current location (Want et al. 1992)
  Sending printouts to nearest printer, displaying files specific to user’s location (Schilit et al. 1999)
Location is one of the most important components of user context
  Allows also infering additional pieces of context (user activity, mode of transportation, social relationships)
No single location technology is accurate, low-cost, easy to deploy and ubiquitous
  Typically tradeoff between accuracy, coverage and cost

## Slide 8: Location representation
Location can be represented in absolute, relative or symbolic form
  Absolute: exact position such as address or GPS coordinates
  Relative: St Kilda is 3 km south of Melbourne
  Symbolic: home, work, bedroom, beach, etc.
Geographic coordinates: latitude and longitude
University of Melbourne:
37°47'49.1"S, 144°57'44.5"E

## Slide 9: Infrastructure and client-based location systems
Client-based location system
  Device computes its own location
  Example: GPS
  Main advantage: preserves location privacy of the device
Network-based location system
  Network infrastructure calculates position of device
Network-assisted location system
  Both device and network infrastructure participate in computing location
  Example: A-GPS

## Slide 10: Approaches to determining location (1)
Proximity
  Location is estimated from closeness of device to reference point
  Example: proximity to a wireless AP
Trilateration
  Position of device is computed from distances between device and reference points at known locations
    Number of reference points = number of physical space dimensions + 1
  Time of flight
    Requires clock synchronization between reference points
  Signal strength attenuation
    Signal attenuation model
    Subject to complex interactions with physical environment

## Slide 11: Approaches to determining location (2)
Hyperbolic lateration
  Difference between signal arrival times (TDOA) at two reference points defines location of device as hyperbolic line
Triangulation
  Location is estimated from angle of arrival (AOA) of signals between device and reference points
  Estimation of AOA requires directional antenna or antenna array, thus AOA is typically measured at reference points (not at device)

## Slide 12: Approaches to determining location (3)
Fingerprinting
  RF fingerprinting relies on two properties of radio signals: temporal stability and spatial variability
  In training phase RF measurements (”fingerprint”) are captured from target environment (spatial resolution vs positioning accuracy)
  Location estimate is obtained by comparing current RF measurement to training measurement
  Measurements by device, location computations by device or infrastructure
Dead reckoning
  Location is computed from previously known location (fix), elapsed time, direction and average speed of movement

## Slide 13: Error reporting
Sources of errors
  Incorrect reference point coordinates
  Ionospheric and tropospheric delay
  Clock synchronization
  Multipath propagation
  Geometry
Reporting error
  Symbolic locations: confidence intervals (correct 85% of the time)
  Absolute locations: cumulative distribution function of location error

## Slide 14: Location systems (some obsolete)

## Slide 15: Example modern positioning system: Infsoft

## Slide 16: Comparison of indoor positioning systems (Batistic & Tomic, 2018)

## Slide 17: Smart floor

## Slide 18: In-home localisation

## Slide 19: Sensing via air pressure

## Slide 20: Break! – 15 minutes
During the break, please complete the questionnaire at:
http://go.unimelb.edu.au/jb8r

## Slide 21: Selected examples of research on location-aware systems

## Slide 22: SmartLibrary (2003)
One of the first examples
  Adaptation of existing service for various mobile devices
    Automatic UI adaptation based on HTTP user agent
  Optional map-based guidance
    WLAN positioning of the device based on RF fingerprint
  Motivation
    To provide mobile access to library database
    To assist library users in finding books by themselves
      Users not familiar with the shelf classification system overload the library staff with their requests for guidance

## Slide 23: SmartLibrary version 1
Separate client application for WLAN positioning of the PDA
"Raw" graphics
In user evaluation map-based guidance to books proved useful, especially to novice library patrons
  Usefulness of dynamic relative user positioning remained doubtful
Aittola M, Ryhänen T & Ojala T (2003) SmartLibrary - Location-aware mobile library service. Proc. Mobile HCI 2003, Udine, Italy, 411-416.

## Slide 24: SmartLibrary version 2
Pure web-based (XHTML) browsing UI
Web CPI (Content Provider Interface) for content management
  Other library resources included, in addition to books
Improved graphics
  Had to create floorplans for the whole university :)
Aittola M, Parhi P, Vieruaho M & Ojala T (2004) Comparison of mobile and fixed use of SmartLibrary. Proc. Mobile HCI 2004, Glasgow, Scotland, 383-387.

## Slide 25: panOulu WiFi
Slide
November 13, 2014

## Slide 26: Reconstructing movement
Slide
November 13, 2014

## Slide 27: Where is it busy now?

## Slide 28: Catchment areas

## Slide 29: Induction loops

## Slide 30: Smarter traffic lights

## Slide 31
Operating theatre tracking
Track patients/staff in & out of operating theatres

## Slide 47: Summary
Characterizing location technologies
  Location representation
  Infrastructure and client-based location systems
  Approaches to determining location
  Error reporting
Location systems